## Slide 1: Update on BRSKI-AE – Support for asynchronous enrollment
draft-ietf-anima-brski-async-enroll-03
Steffen Fries, Hendrik Brockhaus, Elliot Lear, Thomas Werner
IETF 111 – ANIMA Working Group

## Slide 2: Problem to solve
Limited or no connectivity between Pledge and Registrar.
Distinction between operational modes of the pledge
  Pledge-initiator-mode (use case 1): Pledge acts as client and follows the BRSKI approach for the voucher exchange, but allows for alternative enrollment protocols
  Pledge-responder-mode (use case 2): Pledge acts as server and communicates with registrar via a registrar-agent. Pledge is triggered (pushed) to generate and receive bootstrapping data.  main changes made this use case
Draft addresses these issues by defining the call flow and objects to be exchanged. To be independent of the transport security authenticated self-contained objects (signature-wrapped objects) for the certificate enrolment to bind proof of possession and poof of identity to the exchanged objects (similar to existing voucher exchanges with pledge)
7/9/2021
2

## Slide 3: BRSKI-AE Status History of (main) changes from version 01 to version 02
Defined detailed call flow and exchanged objects for interactions in UC2 between pledge – registrar-agent – registrar and MASA. Object format aligns with draft JOSE signed voucher artifacts (Section 5.2.3).
Removed TLS-PSK approach between pledge and registrar-agent to allow transport security independent object exchange and also to avoid relying on PSK.
Included enhancements in voucher-request content and handling to allow registrar to verify agent-proximity to the pledge (enhancements in voucher-request and handling on registrar) in Section 5.2.3.
Defined enhancements in voucher-request YANG to allow for additional parameters to be transported (Section 6).
Terminology alignment (pledge-agent -> registrar-agent; PULL/PUSH -> pledge-initiator-mode and pledge-responder-mode).
7/9/2021
3

## Slide 4: BRSKI-AE Status History of changes from version 02 to version 03
Discussion of open issues discovered in the currently applied YANG definitions:
  YANG doctors were informed to have an early review on
    the enhanced voucher-request from RFC 8995
    the enhancement of the assertion enum of the voucher to include new value agent-proximity (section 5.2)  relates to RFC 8366bis discussion
  YANG module for CSR (for the enrollment request): draft currently reuses SZTP-CSR defined sub module: turns out to be not possible as the complete module must be used.  Proposal provided on mailing list to define ietf-csr-types.yang as part of SZTP-CSR
7/9/2021
4

## Slide 5: BRSKI-AE Status, Use Case 2 Protocol Sketch
Include slides from Michael Richardson to provide overview about the general approach
5
7/9/2021
5

## Slide 6: First Trip
basement

## Slide 7: First Trip
basement
Read device serial number

## Slide 8: First Trip
basement
Alternatively: scan QR Code
Read device serial number

## Slide 9: First Trip
SN: 1234
2021-04-16
basement
LDevID EE (Reg); agent-signed-data in JOSE

## Slide 10: First Trip
Voucher
Request
SN: 1234
LDevID EE (Reg)
Assertion:
agent-proximity
SN: 1234
2021-04-16
basement
voucher request in JOSE

## Slide 11: First Trip
basement
enroll request CSR in JOSE
voucher request in JOSE
Voucher
Request
SN: 1234
LDevID EE (Reg)
Assertion:
agent-proximity
SN: 1234
2021-04-16
Enroll
Request
IDevID
CSR

## Slide 12
Registrar
MASA
basement
service
truck
Domain CA

## Slide 13
basement
service
truck
Registrar
MASA
Domain CA
Voucher
Request
SN: 1234
LDevID EE (Reg)
Assertion:
agent-proximity
SN: 1234
2021-04-16

## Slide 14
Voucher
Request
SN: 1234
LDevID EE (Reg)
Assertion:
agent-proximity
SN: 1234
2021-04-16
Voucher request
basement
service
truck
Registrar
MASA
Domain CA

## Slide 15
basement
service
truck
Registrar
MASA
Domain CA

## Slide 16
basement
service
truck
Registrar
MASA
Domain CA

## Slide 17
basement
service
truck
Registrar
MASA
Domain CA
Enroll
Request
IDevID
CSR

## Slide 18
basement
service
truck
Registrar
MASA
Domain CA
CSR

## Slide 19
basement
service
truck
Registrar
MASA
Domain CA

## Slide 20
basement
service
truck
Registrar
MASA
Domain CA

## Slide 21: Second Trip
basement

## Slide 22: Second Trip
basement
voucher

## Slide 23: Second Trip
basement
voucher
LDevID EE

## Slide 24: BRSKI-AE Status, Use Case 2 Verification of agent-proximity
Data exchange between registrar-agent and pledge based on signed objects (no TLS)
Enhancements in pledge voucher-request with a signed statement from registrar-agent
Allows registrar to identify, which registrar-agent is involved in the bootstrapping
Registrar includes LDevID EE(RegAgt) into registrar-voucher-request.
As pledge-voucher-request is included in registrar-voucher-request MASA can also verify agent-proximity and trust relation registrar-agent / registrar
MASA can issue assertion “agent-proximity”, which is weaker than “proximity” but stronger than “logged” or “verified”
  "agent-proximity" is a statement that the proximity-registrar-certificate was provided via the registrar-agent and that the pledge could not verify proof-of-possession at the time of voucher-request creation
  “proximity” is a statement that the proximity-registrar-certificate was received directly (via TLS) and that the pledge could verify proof-of-possession during the TLS handshake before voucher-request creation.
24
7/9/2021
24

## Slide 25: Discussion, open issues
Version 03 addresses most of the existing issues in the github/anima-wg
Current open issues
  Early review of enhanced voucher-request in section 6
  #10: YANG module for CSR to be used in enrollment-request
  #18: enhancement of YANG voucher with new assertion “agent-proximity”  discussion in the context of revising RFC 8366 to allow for enhancements of assertion types
25
7/9/2021
25

## Slide 26: Next Steps
Clarification of open issues stated in github/anima-wg and also in the draft
Circulate outcome on the mailing list for further discussion
WG review appreciated

## Slide 27: Backup
27

## Slide 28: BRSKI-AE, Use Case 2 Abstract Protocol Overview
Trigger Voucher-request { {reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Basement no connectivity to backend
First floor, connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
Domain CA
MASA
Trigger Enrollment-request
Enrollment-request {signature wrapped CSR}
Voucher {reg-cert, assertion, …}
Voucher-status
Enrollment-response {LDevID Cert}
Enrollment-status
Enrollment-request (CSR)-request
Enrollment-response (LDevID Cert)
IDevID
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
28
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher and LDEvID cert to pledge

## Slide 29: Old slides (IETF 110)

## Slide 30: BRSKI-AE Status, Use Case 2 Trust Establishment (Pledge/Pledge-agent/Registrar)
<<<
<<
+--------------Drop Ship-------------------------------------------------------------------------------------+
| |
V |
+--------+ +-------+ .............................|......... |
| | | | . | . |
| | | | . +-----------+ +-----v-----+ . +------------------------+
| | |Pledge | . | | | | . | Vendor Service |
|Pledge(-| | Agent | . | Join | | Domain | . +------------------------+
|callee) | | | . | Proxy | | Registrar | . BRSKI- MASA | M anufacturer| |
| <-------------->.......<--------------->...........<-------> (PKI RA) <----------------------> A uthorized |Ownership|
| BRSKI-AE/PUSH | BRSKI-AE . | BRSKI-AE | | . | S igning |Tracker |
| | | | . | | +-----+-----+ . | A uthority | |
|IDevID | | | . +-----------+ e.g. RFC7030 . +------------------------+
| | |LDevID | . +-----------------+------+ .
| | | | . | Key Infrastructure | .
| | | | . | (e.g., PKI Certificate | .
+--------+ +-------+ . | Authority) | .
. +------------------------+ .
.......................................
"Domain" components
Trigger Voucher-request {reg-cert}
Voucher-request {S/N, reg-cert, …}
Voucher-request {S/N, reg-cert, …}
Optional S/N verification
S/N verification
Verification „reg-cert“ in voucher is own cert
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with agent-provided-registrar-cert assertion
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Signed objects over http
Signed objects over TLS
Signed objects over TLS

## Slide 31: BRSKI-AE Status, Use Case 2 Trust Establishment (Pledge/Pledge-agent/Registrar)
Alternative proposal not using TLS between the pledge and the pledge-agent under the following assumptions
  the TLS connection for DoS protection only necessary for the registrar endpoints
  the registrar certificate is always included in the voucher request
  the registrar and the MASA verify the certificate contained in the voucher-request (besides further verification like the serial number of the pledge)
Pledge-agent communicates with the pledge via plain http and provides registrar certificate to the pledge
Pledge constructs voucher-request, includes registrar certificate, signs with IDevID
Pledge-agent may verify the pledge serial number in the IDevID by information provided upfront QR code from the pledge and forwards voucher-request via https to registrar
Registrar verifies pledge serial number and its own certificate as part of the voucher-request

## Slide 32: BRSKI-AE Status, Use Case 2 Trust Establishment (Pledge/Pledge-agent/Registrar)
Alternative proposal not using TLS between pledge and pledge-agent
DoS protection only for registrar endpoints  TLS between pledge-agent and registrar
Registrar certificate provided by pledge-agent to be included in the voucher-request  included in the (IDevID signed) voucher-request as new leaf “agent-provided-registrar-cert”
Enables the registrar (am I the right one) and the MASA verify the certificate contained in the voucher-request (besides further verification like the serial number of the pledge)  could use existing voucher assertion "verified" or "logged", or define a new assertion
Pledge-agent may verify pledge serial number in voucher-request with information provided upfront
Registrar verifies pledge serial number and its own certificate as part of the voucher-request
What do we loose? Proximity to registrar via mutually authenticated TLS (and assertion in voucher).
What do we gain? Flexibility in the bootstrapping approach by keeping the number of roundtrips.
Thoughts?

## Slide 33: BRSKI-AE Status, Use Case 2 Trust Establishment (Pledge/Pledge-agent/Registrar), cont.
Trust Establishment between the pledge-agent and registrar may be with LDevID of pledge-agent (could be provided through an independent BRSKI run or by manual task). Enables distinction on the registrar side if a pledge connects or a pledge-agent.
Pledge-agent provides registrar certificate to pledge for inclusion into voucher-request provides the registrar to verify, it gets a voucher-request for a pledge to be bootstrapped and if it is the correct registrar. (see also slide before)
Discussion in the design team regarding a potential authorization token, which is provided in a pre-run to the pledge-agent and then forwarded to the pledge for inclusion into the voucher-request, to be checked by the registrar during voucher-request verification, but was not further followed.

## Slide 34: BRSKI-AE Status, Use Case 2 Pledge endpoints, content types, and objects
Endpoints on pledge and potential object types (current state of discussion, first concrete example):
  /triggervoucherrequest: initiates pledge(-callee) voucher request creation, potentially with additional information (e.g., registrar certificate)  application/json returns pledge(-callee) voucher request  to be discussed: e.g., JOSE object (application/voucher-jose+json)
  /supplyvoucherresponse: provide voucher response to pledge(-callee)  to be discussed: e.g., JOSE object like the voucher-request (application/voucher-jose+json) returns pledge(-callee) voucher status  to be discussed: e.g., JWS
  /triggerenrollrequest: initiates pledge(-callee) certification request creation  application/json returns certification request  PKCS#10-signed-with-IDevID (Format: e.g., JWS)
  /supplyenrollresponse: provide domain credentials to pledge(-callee)  application/pkcs7-smime; smime-type=certs-only returns pledge(-callee) enroll status  to be discussed: e.g., JWS
Note that the object types need to be aligned with the existing object types on the registrar.

## Slide 35: BRSKI-AE Status, Use Case 2 Terminology discussion
Pledge-agent vs. Registrar-agent
  As the agent is intended to provide the interface to the registrar and also to be manufacturer independent, a better naming may be indeed registrar-agent.
  Any objection to the renaming?
PULL/PUSH
  Currently used to distinguish between pledge acting as client or server.
  Better naming to ensure no confusion with the communication direction and other components requested.
  Alternative may be client/server mode for the pledge or pledge-initiated/agent initiated bootstrapping
  Thoughts?
+------------------------+
+--------------Drop Ship---------------| Vendor Service |
| +------------------------+
| | M anufacturer| |
| | A uthorized |Ownership|
| | S igning |Tracker |
| | A uthority | |
| +--------------+---------+
| ^
| | BRSKI-
V | MASA
+--------+ +-------+ .............................|.........
| | | | . | .
| | | | . +-----------+ +-----v-----+ .
| | |Pledge | . | | | | .
|Pledge(-| | Agent | . | Join | | Domain | .
|callee) | | | . | Proxy | | Registrar | .
| <----->.......<-------->...........<-------> (PKI RA) | .
| BRSKI-AE/PUSH |BRSKI-AE| BRSKI-AE | | .
| | | | . | | +-----+-----+ .
|IDevID | |opt. | . +-----------+ e.g. RFC7030 .
| | |IDevID | . +-----------------+------+ .
| | |or | . | Key Infrastructure | .
| | |LDevID | . | (e.g., PKI Certificate | .
+--------+ +-------+ . | Authority) | .
. +------------------------+ .
.......................................
"Domain" components
Note: Join Proxy may be optional, depending on pledge-agent configuration or registrar discovery