## Slide 1
Update on BRSKI-AE: Alternative Enrollment Protocols in BRSKI
draft-ietf-anima-brski-ae-06
Repo URL: https://github.com/anima-wg/anima-brski-ae
David von Oheimb (ed.), Steffen Fries, Hendrik Brockhaus
Shepherd: Toerless Eckert
IETF 118 – ANIMA Working Group

## Slide 2
BRSKI-AE status: recent activity
WGLC ended April 3rd; all comments and suggestions addressed before IETF 117
Open issue:
  Discovery of registrars with BRSKI-AE capabilities
Proposed approach (Design Team):
  In engineered environments, use discovery as specified in RFC 8995, assuming a-priori knowledge of functionality and supported enrollment protocol.
  For heterogeneous scenarios, a more general solution is being defined: BRSKI-Discovery
  This avoids extra requirements and implementation effort regarding discovery in simple cases and allows finalization of BRSKI-AE and further BRSKI enhancements, while referencing a more versatile approach.
Changelog from version 05 to 06:
  Extend section on discovery according to discussion in the BRSKI design team
  Make explicit that MASA voucher status telemetry is as in BRSKI
  Add a note that on delegation, RA may need info on pledge authorization
Notes: 2

## Slide 3
Done already for IETF 115:
  IETF PoC implementation ✓
  WG review done by Michael Richardson ✓
  Document shepherd review done by Toerless Eckert ✓
Done already for IETF 116:
  SECDIR early review ✓
WGLC ended on April 3rd ✓
document shepherd writeup ✓
Still open: finalize section on discovery of registrars with BRSKI-AE feature set
Thereafter, will be ready for AD review
BRSKI-AE status: waiting for outcome on BRSKI discovery
Notes: 3

## Slide 4
TLS with provisional accept of registrar certificate
Accept registrar certificate
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification of pledge signature and IDevID (pledge)
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with assertion proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Pledge (caller)
Domain Registrar, RA / LRA / enrollment proxy
PKI CA
MASA
Certification request (self-contained)
Certification response (LDevID cert)
IDevID
Manufacturer trust anchor
LDevID (Reg)
IDevID Cert CA
S/N Pledge
PKI CA credentials
MASA credentials
Initial steps: Voucher request/response handling as in BRSKI
Adapted step: Using alternative enrollment protocol (e.g., Lightweight CMP)
Request CA certificates (opt.)
CA certificates (opt.)
Request certificate attributes (opt.)
Certificate attributes (opt.)
Verification of LDevID cert
Any remaining verification of request and authorization
Voucher-status
Enrollment-status
PKI RA
PKI RA credentials
Full / partial / no processing of request
Device audit log
BRSKI-AE: abstract protocol overview
Certificate confirmation (opt.)
PKI/Registrar conformation (opt.)
Notes: 4